## Slide 1: Programmable HPC Network Fabrics for Adaptive Computing
Dr. Venkat Dasari
Army Research Laboratory
Supercomputing 2017
Approved for public release

## Slide 2: Motivation
Rapid adoption of heterogeneous computing platforms require hardware independent abstraction layer to connect data to the computing platforms.
Adaptive computing architectures are highly needed in tactical environment
Network is also a computer.
Approved for public release

## Slide 3: Adaptive Computing Overview
Heterogeneous computing platforms
Hardware agnostic AIML abstractions
Programmable Networks
Approved for public release

## Slide 4
Classical vs Programmable Networks
Control plane is externally placed in programmable networks.
Networks are application aware and vice versa
Unified forwarding and Security Policy enforcement
Software driven network intelligence and vendor agnostic
Approved for public release

## Slide 5
Design Overview
MPI/OpenFlow Interaction Schema extended from Takahashi, et al. model
Global view of HPC programmable network fabric
Approved for public release
Notes: Add more descriptive labels

## Slide 6
Approach
  Modify OpenFlow switch and controller
  Modify Ryu, build and install with additional MPI fields
  Modify Open VSwitch
  Modify Loxigen, build OpenFlow Dissector
  Install kernel modules and binaries for testing with Mininet
Approved for public release

## Slide 7
Proposed MPI Data Structures for OpenFlow
 | CPU load | RAM load | Bandwidth | Latency
Description | Current total CPU load % on node | Current total RAM load % on node | Current % of total throughput available | Round trip time between switch and node
Field Name | mpi_cload | mpi_rload | mpi_bwidth | mpi_ping
New data structures proposed to create interaction between OpenFlow and MPI
Approved for public release

## Slide 8
Code Snippet
Programmable OpenFlow functions
Approved for public release

## Slide 9
Experimenter labels captured
Approved for public release

## Slide 10
Adaptive Computing Cluster
Real-time visualization of programmable network fabric for adaptive computing
Approved for public release
Chart: Effect of slicing on throughput between a pair of nodes
| Unsliced Network | Sliced Network
 | 17.9 | 31.9

## Slide 11
DEMO
Approved for public release